## Slide 1
PEK-190
Permanent Magnet Synchronous Motor
(PMSM) Drive

## Slide 2
Introduction of PMSM Principle, Inverter Drive Hardware Circuit and Digital Control Developing Platform Provided by PSIM
Lab 1: Vector Control of PMSM
Lab 2: Initial Angle Detection and Starting of PMSM
Lab 3: Parameter Measurement and Identification of PMSM
Lab 4: Position Sensor-less Control of PMSM with Sliding Mode Observer (SMO)
Lab 5: Position Sensor-less Control of PMSM with Self-adaptive Sliding Mode Observer
Lab 6: Position Sensor-less Control of PMSM with Model Reference Adaptive System (MRAS) Observer
Contents

## Slide 3
PSIM and Its Digital Control Platform
Introduction

## Slide 4
PSIM Functions

## Slide 5
Digital Control Implementation
(On-line tuning of control parameters)
SimCoder + TI DSP Target

## Slide 6
PSIM SimCoder
The element with CG and TI on the left column of the element can be used for code generation

## Slide 7
System in Continuous Domain
System with SimCoder for Code Generation of Hardware Target
System in Discrete Domain
Code Generation - A Step-by-Step Approach

## Slide 8
#include<math.h> #include"PS_bios.h" typedef float DefaultType; #defineGetCurTime() PS_GetSysTimer() interrupt void Task(); DefaultTypefGbliref = 0; DefaultTypefGblU2 = 0; interrupt void Task() { DefaultTypefU2, fSUMP1, fSUMP3, fk3, fk1, fSUM1, fZ1, fTI_ADC1, fVDC2; PS_EnableIntr(); fU2 = fGblU2;
fTI_ADC1 = PS_GetDcAdc(0);
fVDC2 = 2;
fZ1 = fTI_ADC1;
fSUM1 = fVDC2 - fZ1;
fk1 = fSUM1 * 0.4;
fk3 = fSUM1 * (1000.0/20000);
fSUMP3 = fk3 + fU2;
fSUMP1 = fk1 + fSUMP3;
PS_SetPwm1RateSH(fSUMP1);
#ifdef_DEBUG
fGbliref = fVDC2;
#endif
fGblU2 = fSUMP3;
PS_ExitPwm1General();
}
void Initialize(void)
{
PS_SysInit(30, 10);
PS_StartStopPwmClock(0);
PS_InitTimer(0, 0xffffffff);
PS_InitPwm(1, 0, 20000*1, (4e-6)*1e6, PWM_POSI_ONLY, 42822);// pwnNo, waveType, frequency, deadtime,
outtype
PS_SetPwmPeakOffset(1, 10, 0, 1.0/10);
PS_SetPwmIntrType(1, ePwmIntrAdc0, 1, 0);
PS_SetPwmVector(1, ePwmIntrAdc0, Task);
PS_SetPwmTzAct(1, eTZHighImpedance);
PS_SetPwm1RateSH(0);
PS_StartPwm(1);
PS_ResetAdcConvSeq();
PS_SetAdcConvSeq(eAdc0Intr, 0, 1.0);
PS_AdcInit(1, !1);
PS_StartStopPwmClock(1);
}
void main()
{
Initialize();
PS_EnableIntr(); // Enable Global interrupt INTM
PS_EnableDbgm();
for (;;) {
}
}
Code Generation
這一部分電路將會被轉成 C code

## Slide 9
F28335 DSP Port Assignments (Pin 1 - 88)

## Slide 10
F28335 DSP Port Assignments (Pin 89 - 176)

## Slide 11
 | pin |  | 
+5V in | 1 | 2 | +5V in
GND | 3 | 4 | GND
GPIO-00 / EPWM | 5 | 6 | GPIO-01 / EPWM-1B / MFSR-B
GPIO-02 / EPWM | 7 | 8 | GPIO-03 / EPWM-2B / MCLKR-B
GPIO-04 / EPWM | 9 | 10 | GPIO-05 / EPWM-3B / MFSR-A / ECAP-1
GPIO-06 / EPWM / SYNCI / SYNCO | 11 | 12 | GPIO-07 / EPWM-4B / MCLKR-A / ECAP-2
GPIO-08 / EPWM / CANTX-B / ADCSOC-A | 13 | 14 | GPIO-09 / EPWM-5B / SCITX-B / ECAP-3
GPIO-10 / EPWM / CANRX-B / ADCSOC-B | 15 | 16 | GPIO-11 / EPWM-6B / SCIRX-B / ECAP-4
GPIO-48 / ECAP5 / XD31 (EMIF) | 17 | 18 | GPIO-49 / ECAP6 / XD30 (EMIF)
GPIO-84 | 19 | 20 | GPIO-85
GPIO-12 / TZ1n / CANTX-B / MDX-B | 21 | 22 | GPIO-13 / TZ2n / CANRX-B / MDR-B
GPIO-15 / TZ4n / SCIRX-B / MFSX-B | 23 | 24 | GPIO-14 / TZ3n / SCITX-B / MCKX-B
GPIO-24 / ECAP1 / EQEPA-2 / MDX-B | 25 | 26 | GPIO-25 / ECAP2 / EQEPB-2 / MDR-B
GPIO-26 / ECAP3 / EQEPI-2 / MCLKX-B | 27 | 28 | GPIO-27 / ECAP4 / EQEPS-2 / MFSX-B
GPIO-16 / SPISIMO-A / CANTX-B / TZ-5 | 29 | 30 | GPIO-17 / SPISOMI-A / CANRX-B / TZ-6
GPIO-18 / SPICLK-A / SCITX-B | 31 | 32 | GPIO-19 / SPISTE-A / SCIRX-B
GPIO-20 / EQEP / MDX-A / CANTX-B | 33 | 34 | GPIO-21 / EQEP1B / MDR-A / CANRX-B
GPIO-22 / EQEP1S / MCLKX-A / SCITX-B | 35 | 36 | GPIO-23 / EQEP1I / MFSX-A / SCIRX-B
GPIO-28 / SCIRX-A / -- / TZ5 | 37 | 38 | GPIO-29 / SCITX-A / -- / TZ6
GPIO-30 / CANRX-A | 39 | 40 | GPIO-31 / CANTX-A
GPIO-32 / I2CSDA / SYNCI / ADCSOCA | 41 | 42 | GPIO-33 / I2CSCL / SYNCO / ADCSOCB
ADCIN-B7 | 43 | 44 | ADCIN-A7
ADCIN-B6 | 45 | 46 | ADCIN-A6
ADCIN-B5 | 47 | 48 | ADCIN-A5
ADCIN-B4 | 49 | 50 | ADCIN-A4
ADCIN-B3 | 51 | 52 | ADCIN-A3
ADCIN-B2 | 53 | 54 | ADCIN-A2
ADCIN-B1 | 55 | 56 | ADCIN-A1
ADCIN-B0 | 57 | 58 | ADCIN-A0
GND | 59 | 60 | GND
RS232
JTAG
I/O Interface
DSP Control Board I/O Interface

## Slide 12
SimCoder Elements for TI F2833X Hardware Target
PWM generators: 3-phase, 2-phase, 1-phase, and APWM
Variable frequency PWM
Start/Stop functions for PWM generators
Trip-zone and trip-zone state
A/D converter
Digital input and output
SCI configuration, input, and output
SPI configuration, device, input, and output
CAN configuration, input, and output
Capture and capture state
Encoder and encoder state
Up/Down counter
Interrupt time
DSP clock
Hardware configuration

## Slide 13
SimCoder Elements for TI F28335 Target
PWM

## Slide 14
A/D Converter
Digital I/O
SCI
SPI
CAN

## Slide 15
Capture
Encoder
DSP Configuration
PSIM Simulation Control

## Slide 16
PEK-190
Hardware Introduction

## Slide 17
Experimental System
PEK-190 Motor Drive
PTS-1000
M-G Set

## Slide 18
330uF
DC
Voltage
+
-
VDC+
VDC-
Gate Drive
PWM1A
(GPIO0)
PWM1B
(GPIO1)
PWM2A
(GPIO2)
PWM2B
(GPIO3)
Start/Stop
PWM
GPIO49
Vdc
+
Vdc
-
Ks=1/3.3375
Push
bottom
Kv=1/71.556
ADC-A0(AC)
ADC-
B0(DC)
Q1
Q2
Q3
Q4
CPLD
F28335
DSP
Protection
Circuit
RS232
SCIC
(GPIO 62, 63)
Q5
PWM3A
(GPIO4)
PWM3B
(GPIO5)
Q6
Isa
Isb
Isc
ADC-A1(AC)
ADC-A2(AC)
Voa
Vob
To Motor
Voc
Q7
R
PWM4A
(GPIO6)
A, B, Z
DC Source
From Encoder
(GPIO 20, 21, 22, 23)
Inverter I/O Configuration

## Slide 19
MOSFET
DC
Capacitor
F28335 DSP
Control Board
Gate Drive
Circuit
Test Points
RS232
JTAG
Hall
Current Sensor
ON/OFF
Push Bottom
PEK-190 Outlook

## Slide 20
Test Points
Q1, Q2, Q3, Q4, Q5: PWM signal
Isa, Isb, Isc: sensor factor = 1/3.3375
Vdc: sensing factor = 1/71.556

## Slide 21
Encoder
DC
Voltage
Auxiliary Power Supply
Input
Hall Sensor Input
Motor Connection
Connections

## Slide 22
Main Power Circuit

## Slide 23
Voltage and Current Sensing Circuits

## Slide 24
Interface Circuit

## Slide 25
Encoder Feedback Circuit

## Slide 26
26
DSP Control Board (with Isolated RS232 port)
Flyback Auxiliary Power Supply
JTAG Module
Auxiliary Circuits
Switch Drive Power and Drive Circuit

## Slide 27
27
Gate Drive Power Circuit
Gate Drive Circuit
12V Input(Isolated)
GND
VIN+(PWM_outA)
VIN-(PWM_outB)
VIN+(+12V)
VIN- (-12V)
Photo couple MOSFET Driver
From PWM
(CPLD)
UC3845
DRV8800
VIN+(PWM_outA)
VIN-(PWM_outB)
50kHz
Gate Drive
Voltage
ON: +12V
OFF: -3.3V
12Vdc
UC3845 is used to generate
50KHz CLK signal for DRV8800

## Slide 28
DRV8800 IC
To Generate 12V square wave voltage for gate drive power
It can provide 2.8A output current
+12V
To Gate Drive Circuit
VIN+(PWM_outA)
VIN-(PWM_outB)

## Slide 29
USB_JTAG Circuit
ISO7240
ISO7242

## Slide 30
Auxiliary Power Supply (Flyback with multiple outputs and linear regulators)
+15V
-15V
+5V
GND
AC Input
90Vac~264Vac
+12V(Isolated)

## Slide 31
PMSM
Introduction

## Slide 32
Structure of PMSM
Surface Mounted PMSM
Interior PMSM

## Slide 33
PMSM Motor-Generator Set (400W, 3000rpm)

## Slide 34
PMSM state equations in abc-axis
：rotor flux linkage
PMSM Equivalent Circuit

## Slide 35
PMSM Equivalent Circuit Model in abc-axis

## Slide 36
Axis Transformation
dqo to abc
abc to dqo

## Slide 37
abc to αβ
αβ to abc
Clarke and Inverse Clarke Transformation

## Slide 38
dq to αβ
αβ to dq
Park and Inverse Park Transformation

## Slide 39
R
Ld
-weLqIq
+
Ud
-
Id
R
Lq
we(LqIq+ff)
+
Uq
-
Iq
pn is the motor pole-pair number
(rpm)
(rad/s)
DQ-axis Equivalent Circuit Model of PMSM

## Slide 40
Prated=400W, Nrated=3000rpm
Trated=1.27Nm (=P,rated/wm,rated)
R = 1.55W, Lq=Ld=6.71mH
J = 27.7u, Shaft time constant (J/B) = 0.53
Pole = 10
Vf = Vpk/krpm = 17.4 * 1.414
Experimental Motor
=314.16(rad/s)
(P/2) * =1570.8(rad/s)

## Slide 41
Motor Parameters in PSIM

## Slide 42
Three-phase Sinusoidal PWM (SPWM)

## Slide 43
Space Vector PWM (SVPWM)
I
II
III
IV
V
VI
V6(110)
V1(001)
V5(101)
V3(011)
V2(010)
V0(000)
V7(111)
a
V4(100)
b

## Slide 44
SVPWM Voltage Vector

## Slide 45
Voltage Vector of the Space Voltage PWM
Vector space can be divided into 6 sections
Vref can be constructed with the adjacent vectors located in the same section and the zero vector
a-axis
b-axis

## Slide 46
Conduction Time Interval of the Voltage Vector (section 1)

## Slide 47
Conduction Time Interval of the Voltage Vectors (section 2~6)

## Slide 48
float PI = 3.1416;
float K1 = 1;
float K2 = 1.732;
float P120=3.1416/3*2;
//0 0~60
if ((x2>0) && (x2<=PI/3))
{
y1 = K1 * x1 * cos(x2 - PI/6);
y3=K1 * x1 * cos(x2 + PI/6 +P120);
y2= K2 * x1 * cos(x2-P120);
}
//1 60~120
if ((x2>PI/3) && (x2<=2*PI/3))
{
y1 = K2 * x1 * cos(x2);
y3= K1 * x1 * cos(x2 - PI/6 +P120);
y2= K1 * x1 * cos(x2 + PI/6-P120);
}
//2 120~180
if ((x2>2*PI/3) && (x2<=PI))
{
y1 = K1 * x1 * cos(x2 + PI/6);
y3= K2 * x1 * cos(x2+P120);
y2= K1 * x1 * cos(x2 - PI/6-P120);
}
//3 180~240
if ((x2>-PI) && (x2<=-2*PI/3))
{
y1 = K1 * x1 * cos(x2 - PI/6);
y3= K1 * x1 * cos(x2 + PI/6+P120);
y2= K2 * x1 * cos(x2-P120);
}
//4 240~300
if ((x2>-2*PI/3) && (x2<=-PI/3))
{
y1 = K2 * x1 * cos(x2);
y3= K1 * x1 * cos(x2 - PI/6+P120);//y2= K2 * x1 * cos(x2+P120);
y2= K1 * x1 * cos(x2 + PI/6-P120);
}
//5 300~360
if ((x2>-PI/3) && (x2<=0))
{
y1 = K1 * x1 * cos(x2 + PI/6);
y3= K2 * x1 * cos(x2+P120);
y2= K1 * x1 * cos(x2 - PI/6-P120);
}
Real Implementation of SVPWM
SVPWM
Control
Voltage
Calculation

## Slide 49
SVPWM Simulation
SVPWM (black)
SPWM(red)

## Slide 50
PMSM
3-Phase
Inverter
Speed
Controller
Current
Controller
Axis
Transformation
abc-to-dq
SVPWM
Encoder
pn
+
-
wm
we
Speed
Calculator
A, B, Z
wmc
isa
isb
isc
iq
id
iqc
idc=0
vconq
vcond
Q1~Q6
Gate
Drive
G1~G6
wm
Load
Te
TL
wm
Lab 1: Vector Control of PMSM

## Slide 51
1
2
where
Kpwm: Inverter voltage gain
Vtm : the amplitude of PWM triangular waveform
ks: current sense gain
Current Loop Control Scheme
Feedback + Feedforward Control
GI : PI + LPF = Type 2 regulator
Id
Iq
Vcond
Vconq
idc
(=0)
iqc
id
iq
+
+
+
+
+
+
+
+
-
-
ks
ks
LPF
LPF
1
2
Vffd
Vffq

## Slide 52
Set uI to be 1/8~1/10 of the switching frequency(fs)
Set z = uI/3
Set p = fs/(4p)
Find K
uI
z
p
HI
GI
GIHI
Type 2
Current Regulator Design
Bode plot of current loop

## Slide 53
PM
(Phase Margin)
GM
(Gain Margin)
Bandwidth
0dB
-180o
| T |
Low frequency gain
High low-frequency gain for good regulation accuracy
Wide bandwidth for fast response
Enough phase margin PM>45o
Enough gain margin GM>10~20dB
Requirement of Loop Gain

## Slide 54
=
G
H
GH(Loop Gain)
wc
+
-
H
G
KT
1
iq
iqc
Kw
+
-
Speed Regulation
Speed regulator design
Usually PI is adopted as the speed regulator
The crossover frequency (wc) can be assigned to be 1/10 ~ 1/4 of the current loop

## Slide 55
Speed Tracking
+
-
H
G
KT
1
Gf
Kw
iq
iqc
+
-
Feedforward Controller (Gf)

## Slide 56
MT is the peak value of M
MT should be selected so that 1.0 < MT< 1.5
The bandwidth ωBW and the frequency ωp at which MT occurs, should be as large as possible. Large values result in the fast closed-loop responses
Requirement of M

## Slide 57
System Parameters
DC Voltage Vd = 130V
fs = 20kHz, Vtri = 5Vpp (PWM)
Cd = 330uF
Ls = 6.71mH, Rs=1.55W, ff=47m V/rad/s
Ks = 1/3.375 (current sensing factor)
Kv = 1/71.556 (DC voltage sensing), Ks = 1/3.3375 (current sensing)
Max Speed=2000rpm
Max torque = 1.27Nm
P = 10
Kt = 0.3524 Nm/A
Current loop bandwidth fcoi = 750Hz
Speed loop bandwidth fco = 50Hz

## Slide 58
% PMSM Vector Control
clf;
clc;
PI = 3.1416;
% Motor parameters
Po = 400;
Nrated = 3000;
P = 10;
Wmrated = 3000/60 * 2 * PI;
Werated = Wmrated * P/2;
Tn = Po/Wmrated
Ls = 6.71e-3;
Rs = 1.55;
Vf = 17.4 * 1.414 * Nrated/1000;
F = Vf/Werated
J = 0.227e-6;
Tu = 0.53;
B = J/Tu;
Kt = 3/2 * P/2 * F
% Inverter parameters
Vd = 130;
fs = 20e3;
ws = 2 * PI * fs;
ks = 1/3.3375;
kv = 1/71.556;
Vtm = 5;
kpwm = Vd/(2*Vtm);
% current regulator design
% Gi : PI=K1(s+z)/s
p = 10e3 * 2 * PI;
numLR = 1;
denLR = [Ls Rs];
HLR=tf(numLR, denLR);
numLPF = p;
denLPF = [1 p];
LPF=tf(numLPF, denLPF);
Hi = kpwm * ks * series(HLR, LPF);
fcoi = 750
wcoi = 2 * PI* fcoi;
Hir = freqresp(Hi, wcoi);
GainHi = abs(Hir);
z = wcoi/5;
ti = 1/z
numGi1 = [1 z];
denGi = [1 0];
Gi1=tf(numGi1, denGi);
Gi1r = freqresp(Gi1, wcoi);
GainGi1r = abs(Gi1r);
K1 = 1/(GainHi*GainGi1r)
Gi = K1 * Gi1;
GiHi = series(Gi, Hi);
wmin = 100 * 2* PI;
wmax = 50e3 * 2 *PI;
figure(1);
bode(Hi, Gi, GiHi, {wmin, wmax});
grid;
Matlab Controller Design (1/2)

## Slide 59
% Speed regulator design
J = 100e-6;
B = J/Tu;
a = B/J;
b = 1/J;
Kw = 1/100;
numH = Kt/ks * Kw *b;
denH = [1 a];
H=tf(numH, denH);
fco = 75
wco = 2*PI*fco;
Hr = freqresp(H, wco);
GainH = abs(Hr);
z = wco/5;
tw = 1/z
numG1 = [1 z];
denG = [1 0];
G1=tf(numG1, denG);
G1r = freqresp(G1, wco);
GainG1r = abs(G1r);
K2 = 1/(GainH * GainG1r)
G = K2 * G1;
GH = series(G, H);
figure(2);
bode(H, G, GH);
grid;
% Speed tracking controller design
p = 100;
z = 250;
numGf = p/z * [1 z];
denGf = [1 p];
Gf=tf(numGf, denGf);
L = GH/(1+GH);
M = Gf * L;
figure(3);
bode(L, M);
grid
Matlab Controller Design (2/2)
Tn = 1.2732
F = 0.0470
Kt = 0.3524
fcoi = 750
ti = 0.001
K1 = 2
fco = 75
tw = 0.01
K2 = 2

## Slide 60
Bode Plot of Current Loop
-80
-60
-40
-20
0
20
40
M
a
g
n
i
t
u
d
e
(
d
B
)
Hi
Gi
GiHi
10
3
10
4
-180
-135
-90
-45
0
P
h
a
s
e
(
d
e
g
)
Current Loop
Frequency (Hz)

## Slide 61
Bode Plot of Speed Regulation Loop
-40
-20
0
20
40
60
80
100
120
M
a
g
n
i
t
u
d
e
(
d
B
)
H
G
GH
10
-2
10
-1
10
0
10
1
10
2
10
3
-180
-135
-90
-45
0
P
h
a
s
e
(
d
e
g
)
Speed Regulation
Frequency (Hz)

## Slide 62
Bode Plot of Speed Tracking Loop
-35
-30
-25
-20
-15
-10
-5
0
5
M
a
g
n
i
t
u
d
e
(
d
B
)
L
M
10
-1
10
0
10
1
10
2
10
3
-90
-45
0
P
h
a
s
e
(
d
e
g
)
Speed Tracking
Frequency (Hz)

## Slide 63
A_sensor1
Simulation Circuit
SVPWM
Axis-transformation
Current controller
Speed controller
Mechanical Load
Equivalent CKT
Motor
Inverter
Inc/Dec
Speed Limiter

## Slide 64
Simulation Result (1/3)
speed(RPM)
Speed feedback and speed command
d-q axis current tracking

## Slide 65
Simulation Result (2/3)
Motor current
q
Real torque(Te) and calculated torque(Tec)

## Slide 66
Simulation Result (3/3)
Motor current
Control voltage (Vcona1) and SVPWM control voltage(Vcona)

## Slide 67
Speed Measurement with Incremental Encoder

## Slide 68
Speed and Angle Calculation(1/2)
Encoder = 2500 ps/rev
Count = =2500 x 4 = 10000 ps/rev

## Slide 69
C1
C2
Ts
(rpm)
Speed and Angle Calculation(2/2)

## Slide 70
Electrical and Mechanical Duality
M
e
T
L
T
m
w
B
J
+
-
The electrical equivalent circuit will be used as to model the mechanical load in PSIM simulation

## Slide 71
Control Circuit Realized with SimCoder
Lab1_sensor1

## Slide 72
Simulation Result (1/3)
Real speed and measured speed(rpm)
Speed and speed command(rad/s)
Dq-axis current tracking

## Slide 73
Simulation Result (2/3)
Motor current
Counter
q
Real torque and calculate torque

## Slide 74
Simulation Result (3/3)
Motor current
SVPWM control voltage

## Slide 75
Lab 2: Initial Angle Detection and Starting of PMSM
By using
Equivalent to
Rotor N pole will be reset to be electrical zero degree
X
X
X

## Slide 76
Simulation Circuit
A_sensor_start1
SVPWM
Axis-transformation
Mechanical Load
Equivalent CKT
Motor
Inverter
Inc/Dec
Speed Limiter
Current controller
Speed controller
Set-zero
controller
Initial position
setting

## Slide 77
Simulation Result
Initial angle
Set zero position
start
angle(q)
Speed(rpm)

## Slide 78
Encoder Counter Reset

## Slide 79
Control Circuit Realized with SimCoder
Lab2_sensor_start1

## Slide 80
Simulation Result

## Slide 81
Lab 3: Parameter Measurement and Identification of PMSM
Rs measure
Rs
Ls(=0)
Rs
Rs
+Ea-(=0V)
+Eb-(=0V)
+Ec-(=0V)
Idc
Idc/2
Idc/2
A
B
C
Vdc
Ls(=0)
Ls(=0)
PMSM
With DC input voltage, motor is in stall, speed voltage is zero and inductance is zero in DC current

## Slide 82
Realization
Vtm is the amplitude of Vtri
Vd
Ks
idcr
Idc
A
B
C
Vtri
0V
0V
Vcona
idc
Vtm
Vtri
N
Precise DC current Idc can be obtained from the closed-loop current control
Vdc can be calculated indirectly from the PWM control voltage Vcona

## Slide 83
Influence of Dead-time to Output Voltage of Inverter-arm

## Slide 84
Factors Needed be Considered in Calculating Rs
Due to Vdc is very small in measuring Rs, it needs to consider the inverter dead-time (td) and voltage droop of inverter switch
Vf
Vd-IdcRds
0.5*IdcRds
Vd+Vf/2
0V
0V
A-Leg
B, C-Leg
VAN
VBN, VCN
Ts

## Slide 85
static float Va, Vb, Rds=0.27, Vf=0.7, Vcon, Ts=50e-6, td=1e-6, vtm=5, Vd=130, Idc=3.3375;
Vcon = x1;
Va = (Vd - Rds * Idc) * ( Ts/2 + Ts * Vcon/(2*vtm) - td) - (Ts/2 + td - Ts * Vcon/(2*vtm) ) * Vf;
Vb = (Vd + Vf/2) * (Ts/2 + td) + Rds/2 * Idc * (Ts/2 - td) ;
y1 = (Va - Vb)/Ts;
R_estimate_1
Simulation Circuit
Compensator
PWM
A-phase current controller

## Slide 86
Simulation Result
1.52W
A-phase current tracking

## Slide 87
Lab3_Estimation_R1
Control Circuit Realized with SimCoder

## Slide 88
Estimation of Ls and ff
In steady-state the derivation of current is zero and Id=0:
1
2
Q-axis model of PMSM
D-axis model of PMSM

## Slide 89
Realization Method for Estimating Ls and ff

## Slide 90
Lab3_Estimation_LF1
Control Circuit Realized with SimCoder
Realization block for estimating Ls and ff

## Slide 91
On-line Mechanical Parameter Estimation
= (
At no load
Electrical equation
Estimation model
Estimation error
Error equation of estimation
J0 and B0 are measured values of the previous sampling time
M
e
T
L
T
m
w
B
J

## Slide 92
Duality of Mechanical to Electrical Model
Realiztion Method for On-line Mechanical Parameter Estimation
M
e
T
L
T
m
w
B
J
+
-
Using AC torque at no-load to estimate the J and B
= (
+
-

## Slide 93
Realization Method
= (

## Slide 94
Lab3_Estimation_Mech1
Control Circuit Realized with SimCoder
Realization block for estimating J and B

## Slide 95
Parameter Identification
Parameters
Adaptive Law
+
-
E
U
i
Reference
Model
Real
PMSM
Adjustable
Model
1
2
1
=
=
2

## Slide 96
Adjustable Model
1

## Slide 97
Adaptive Law
2

## Slide 98
Control Circuit Realized with SimCoder
Lab3_ID_RLF1
MRAS

## Slide 99: PMSM Model Considering Dead-time
Where
Ton/Toff: turn-on and turn-off time of switch
Td: dead-time
Vce0:IGBT conduction voltage droop
Vd0:diode conduction voltage droop
=2

## Slide 100: Rs Estimation with Adaptive Iteration
As iq=0 in steady-state:

## Slide 101
Control Circuit Realized with SimCoder
PEK-190_Estimation_R2

## Slide 102
Simulation Result
Rs=1.48Ω

## Slide 103: Ld and Lq Estimation with Adaptive Iteration
With high-frequency injection of iq and id, motor will not rotate due to the mechanical time constant is large:

## Slide 104
PEK-190_Estimation_L
Control Circuit Realized with SimCoder

## Slide 105
Simulation Result (1/2)

## Slide 106
Ld=6.75mH Lq=6.83mH
Simulation Result (2/2)

## Slide 107: Ѱm Estimation with Adaptive Iteration
In steady-state and no-load condition(id=0):

## Slide 108
PEK-190_Estimation_F
Control Circuit Realized with SimCoder

## Slide 109
Simulation Result (1/2)

## Slide 110
Fm=45.42V/rad
Simulation Result (2/2)

## Slide 111
Lab 4: Position Sensor-less Control of PMSM with Sliding Mode Observer (SMO)
3-Phase
Inverter
Speed
Controller
Current
Controller
SVPWM
+
-
wmE
weE
SMO
1/pn
wmc
isa
isb
isc
iq
id
iqc
idc=0
vconq
vcond
Q1~Q6
Gate
Drive
G1~G6
PMSM
Load
Te
TL
wm
a-b-c
to
a-b
a-b
to
d-q
a-b-c
to
a-b
ia
ib
ua
ub
uc
ua
ub

## Slide 112
Define a surface function
Equivalent Control
Consider the unperturbed system
Sliding Dynamics
SMO Fundamental
Consider the system of the form:
Switching Surface
f(x,t) and d(t) represent the nonlinear uncertainty and external disturbance
The equation (x)=0 defines a linear surface (hyperplane), which is called the switching surface S.
The equivalent control, which is found from the constrains (x)=0 and =0.

## Slide 113
Reaching Control
In case the system states do not locate on the switching surface due to parameter variation and disturbance, an additional control called reaching control should be augmented on the control input to force the system states to reach the switching surface
The condition to guarantee the hitting of trajectory of the system upon the switching surface from arbitrary initial state is

## Slide 114
=
Sliding Mode Observer (SMO)
PMSM Model in a-b
Sliding surface function
Observer
As enter into and stay on the sliding surface, it will be s= ̇
Error equation

## Slide 115
SMO
Sign()
Low-pass
Filter
+
-
+
-
Conventional Angle Calculation Method
Low-pass filter is employed to reduce the switching signal
The low pass filter will introduce a series phase delay of the rotor angle
A compensated angle is required to compensate the angle delay
wc is the cut-off frequency of the low pass filter

## Slide 116
1/s
kd
+
-
S
1/s
Cos()
Sin()
=
Phase-Lock-Loop (PLL)
Equivalent control loop
PLL omit the complex computation of arctan function
It also omit the low-pass filter that may cause a series phase delay

## Slide 117
1/L
1/L
R/L
1/L
1/L
R/L
LPF
LPF
K
K
Cos()
Sin()
1/pn
Ua
Ub
Ia
Ib
qeE
wmE
weE
SMO
PLL
Eae
Ebe
Iae
Ibe
sign
sign
SMO+PLL Speed Observer

## Slide 118
A_sensorless_SMO1
Simulation Circuit
PLL+SMO speed observer

## Slide 119
Simulation Result
Speed (rpm)
Real rotor angle and estimated rotor angle
Dq-axis current tracking
Real current and estimated current in SMO

## Slide 120
Control Circuit Realized with SimCoder
Lab4_sensorless_SMO1
PLL+SMO speed observer

## Slide 121
Simulation Result
Speed (rpm)
Real rotor angle and estimated rotor angle
Dq-axis current tracking
Real current and estimated current in SMO

## Slide 122
3-Phase
Inverter
Speed
Controller
Current
Controller
SVPWM
+
-
wmE
weE
Self-
Adaptive
SMO
1/pn
wmc
isa
isb
isc
iq
id
iqc
idc=0
vconq
vcond
Q1~Q6
Gate
Drive
G1~G6
PMSM
Load
Te
TL
wm
a-b-c
to
a-b
a-b
to
d-q
a-b-c
to
a-b
ia
ib
ua
ub
uc
ua
ub
Lab 5: Position Sensor-less Control of PMSM with Self-adaptive Sliding Mode Observer

## Slide 123
Sliding Mode Observer (SMO)
PMSM Model in a-b
Sliding surface function
Control law
As enter into and stay on the sliding surface, it will be
Error equation

## Slide 124
l
l
-
-
-
+
pn
Self-adaptive
PLL
Self-adaptive Law and PLL
Select Lyapunov function
Stability of the system is guaranteed

## Slide 125
1/pn
Ua
Ub
Ia
Ib
SMO
PLL
Eafe
Ebfe
Iae
Ibe
sign
sign
Cos()
Sin()
qeE
wmE
weE
1/L
1/L
R/L
1/L
1/L
R/L
LPF
LPF
K1
K1
K2
K2
weE
Eaf
Ebf
Self-adaptive
SMO+Self-adaptive+PLL

## Slide 126
Simulation Circuit
A_sensorless_SMO_apt1

## Slide 127
Simulation Result
Speed (rpm)
Real rotor angle and estimated rotor angle
Dq-axis current tracking
Real current and estimated current in SMO
Real speed voltage and estimated speed voltage in SMO

## Slide 128
Control Circuit Realized with SimCoder
Lab5_sensorless_SMO_apt1

## Slide 129
Simulation Result
Speed (rpm)
Real rotor angle and estimated rotor angle
Dq-axis current tracking
Real current and estimated current in SMO
Real speed voltage and estimated speed voltage in SMO

## Slide 130
3-Phase
Inverter
Speed
Controller
Current
Controller
SVPWM
+
-
wmE
weE
MRAS
1/pn
wmc
isa
isb
isc
iq
id
iqc
idc=0
vconq
vcond
Q1~Q6
Gate
Drive
G1~G6
PMSM
Load
Te
TL
wm
a-b-c
to
a-b
a-b
To
d-q
a-b-c
to
d-q
ia
ib
uq
ud
ua
ub
uc
Lab 6: Position Sensor-less Control of PMSM with Model Reference Adaptive System (MRAS) Observer

## Slide 131
Reference
Model
Adjustable
Model
Parameters
Adaptive Law
+
-
E
u
x
Model Reference Adaptive System

## Slide 132
Reference Model
d-q Model of PMSM
Expressed with state equation of current
Rearrange
Reference Model
R

## Slide 133
Adjustable Model
B
Error equation

## Slide 134
According to Popov stability criterion:
H(s)=(sI-Ae)-1 is strictly positive real;
h(0, t1)= is positive and , so MRAS is asymptotically stable
Adaptation Law
Rearrange
(Derived from the solution of Popov inequality)
+
U, I
R
B
PI

## Slide 135
1/L
1/L
R/L
R/L
Ud
Uq
Iq
Id
Ide
Iqe
1/pn
qeE
wmE
weE
weE
Verr
MRAS Realization

## Slide 136
Simulation Circuit
A_sensorless_MARS1

## Slide 137
Simulation Result
Speed (rpm)
Real rotor angle and estimated rotor angle
Dq-axis current tracking
Real current and estimated current in MRAS

## Slide 138
Lab6_sensorless_MARS1
Control Circuit Realized with SimCoder

## Slide 139
Simulation Result
Speed (rpm)
Real rotor angle and estimated rotor angle
Dq-axis current tracking
Real current and estimated current in MRAS

## Slide 140
Thank you for your attention